## Slide 1
TVR (Time-Variant Routing) Applicability draft-zdm-tvr-applicability
Authors L. Zhang
J. Dong Huawei
M. Boucadair Orange
Contributors D. King C. Rotsos Lancaster University P. Liu China Mobile
T. Li
Juniper Networks

## Slide 2: What’ new in this version?
Removed the schedule architecture section
Simplified the use case description
Modified Applicability Section to focus on the following questions:
  In which scenarios TVR data model is applicable?
  How to use TVR data model in these scenarios?
  Added Time Synchronization section
  Added Schedule Database section
  Added Operation Considerations section

## Slide 3: Use Case Examples
Tidal Network Example
  Traffic on the network has an obvious tidal period, including heavy-traffic periods and light-traffic periods
    Network topology change caused by specific traffic pattern.
  The time duration of heavy traffic and light traffic are clearly identifiable
    Students or employees work specific hours
    Network change will occur twice per day
  The switching time between the heavy-traffic period and the light-traffic period is well established
    Working time and day of week are predictable
    Is it sufficient to consider only tidal network use cases in Applicability I-D?
Tidal effect of traffic in campus network

## Slide 4: Applicability of TVR YANG Model in Tidal Network(1/3)
In which scenarios TVR data model is applicable?
Schedule Generation Manner | Schedule Execution Manner | TVR YANG Applicable?
Centralized | Centralized | No
Distributed | Distributed | No
Centralized | Distributed | Yes
Managing Device
Managed Device(s)
Schedule Generation
Schedule Distribution
Schedule Execution

## Slide 5: Applicability of TVR YANG Model in Tidal Network(2/3)
Network model and interactions
Distributed Model
Centralized Model
Interactions:
  Managing device delivers schedules to managed Devices by TVR YANG model.
Interactions:
  Managing device delivers node-specific schedules to network devices by TVR Node YANG module;
  Managing device delivers topology schedules controller by TVR Topology YANG module;
  Network controller delivers routing results to network devices.
Generates and maintains schedules
Execute schedules
Generates and maintains schedules
Calculate routes
Execute schedules and routing results

## Slide 6: Applicability of TVR YANG Model in Tidal Network(3/3)
Encoding of TVR YANG Model
TVR data model defines the following modules:
“ietf-tvr-schedule” module contains the schedule YANG definitions;
“ietf-tvr-topology” module defines a network topology with a time-variant availability schedule;
“ietf-tvr-node” module is to be used to manage the scheduled attributes of a single node.
All of these modules are applicable in Tidal Network to manage devices and deliver topology information.
An JSON example on using “ietf-tvr-node” to shut down a wireless link from 19:00 to 7:00 every day.

## Slide 7: Management Protocols
NETCONF
  Provides a robust mechanism for managing complex network configurations;
  Supports atomic transactions, which ensures schedules involving multiple resources are applied fully, preventing partial updates that could lead to configuration inconsistencies. This is important for TVR environments.
  Supports the validation of configurations prior to commitment, allowing operators to verify the correctness of schedules before they are applied;
RESTCONF
  Provides a simpler, stateless method for interacting with network devices, suitable for use cases requiring lightweight, rapid configuration;
  Provides a streamlined approach to network configuration and management by RESTful interface over HTTP. It has advantages in scenarios where quick adjustments to schedules are needed or where integration with web-based or cloud-native systems is a priority;
  Summary
  NETCONF would be the preferred protocol for large-scale, critical scheduling operations requiring validation and rollback mechanisms.
  RESTCONF would be the preferred protocol for smaller-scale or isolated scheduling tasks.

## Slide 8: Time Synchronization
Hardware-based protocols:
  Rely on dedicated hardware to ensure clock synchronization, such as GPS and Precision Time Protocol (PTP).
  Have higher precision and stability, but also have higher cost due to the dedicated Hardware.
  Appropriate for networks with critical time synchronization scenarios.
Software-based protocols:
  Synchronize clocks through software packages running on systems, such as Network Time Protocol (NTP) and Simple Network Time Protocol (SNTP)
  Simple and applicable to common hardware devices, but have lower precision.
  Appropriate for most of the TVR use cases.

## Slide 9: Time Synchronization in Tidal Network
Time synchronization precision requirements of tidal network : second level.
NTP:
  NTP uses a hierarchical structure of time sources. Each level of this hierarchy is termed a stratum.
  Have higher precision, it can realize the synchronization at tens of milliseconds level.
SNTP:
  SNTP simplifies the complex NTP synchronization function and is suitable for networks with limited resources and loose precision requirements. The synchronization precision still can be guarded under seconds.
  SNTP can be used as an alternative clock synchronization protocol for Tidal Network.
NTP deployment case in tidal network

## Slide 10: Schedule Database
Data Structure
Based on TVR YANG, the schedule database should contain four types of schedule entries.
  Node power schedule entry;
  Interface schedule entry;
  Node schedule entry;
  Links schedule entry;
Schedule Database Requirements
  Schedule database should support the add, update, and delete operations.
  When adding or updating a schedule entry, the execution node needs to check whether resource conflicts exist between the current schedule and existing schedules.
  Schedules are updated and deleted based on schedule IDs. Schedule IDs must be unique in a time-variant domain.

## Slide 11: Operational Considerations
  Coordinated Network Events: TVR often coordinates routing changes anticipating events like predictable link downtimes.
  Accurate Scheduling of Paths: TVR schedule capable nodes will dynamically adjust forwarding paths based on planned changes.
  Time-Stamped Data Models: TVR will require the use time-stamped data to make interface management decisions.
  Schedule Execution Considerations
  A link coming up or a node joining a topology should not have any functional change until the change is proven to be fully operational
  A link or node is to be removed from the topology, then the network should act before the anticipated change to route traffic around the expected topological change.

## Slide 12: Security Considerations
  The "Security Considerations" section of I-D.ietf-tvr-requirements outlines various threat vectors and categories specific to time-variant environments..
  This part will provide detailed security techniques and best practices to address these challenges.
Notes: The integration of time-variant mechanisms in network operations presents distinct security challenges that require thorough analysis to safeguard the network’s integrity, availability, and confidentiality.

## Slide 13: Next Steps
Is only one case sufficient?
Is there any unanswered questions(when, how)?
Welcome for contribution to the operation and security considerations.
Any other questions or suggestions?